## Slide 1: Wisconsin Lane Closure System (WisLCS)
Training

## Slide 2: Introductions
Brian Sippel
WisDOT - BTO
Work Zone Management
(414) 322-4185
Brian.sippel@dot.wi.gov
Scott Kozlik
WisDOT - BTO
STOC
(414) 227-2161
Scott.kozlik@dot.wi.gov
Self-Introductions
Name, LCS experience and role

## Slide 3: Introductions
Brian Sippel
WisDOT - BTO
Work Zone Management
(414) 322-4185
brian.sippel@dot.wi.gov
Chris Quesnell
Lakeside Engineers
BTO Consultant
(262) 789-8200
chris.quesnell@lakesideengineers.com
Self-Introductions
Name, LCS experience and role

## Slide 4: Agenda
Background
Interfaces
Additional LCS Resources
Support Tools
Closure Walk-Through
Activity

## Slide 5: Background
Overview, Roadways, Users, and Regions

## Slide 6: Overview
WisLCS Description:
  BTO Sponsored Tool
  UW TOPS Lab developed system
    WisTransportal System
  Web-based
  Role-based
  Online repository to request, approve, and track lane closures on Interstate, US Highways, and State Highways

## Slide 7: Overview
WisLCS Benefits:
  Facilitate the request, approval, and modifications of lane closure information
  Coordinate activities to reduce delays and potential conflicts
  Eliminate duplications and inefficiencies by streamlining information into one system
  Archive historical data for future use
  Facilitate data sharing

## Slide 8: Overview
WisLCS Use Example:
Wisconsin 511 System http://www.511wi.gov or Dial 5-1-1

## Slide 9: Overview
WisLCS Use Example:
WisDOT Website http://www.dot.wisconsin.gov/travel/road/workzones.htm

## Slide 10: Overview
WisLCS Use Example:
Statewide Traffic Operations Center
STOC Operator Tasks:
DMS Signing
Contact info
Emergency closure entry
Assist project staff with cancellations

## Slide 11: Overview
WisLCS Use Example:
Daily/Weekly E-mail Reports

## Slide 12: Overview
WisLCS Use Example:
FHWA Real-Time System Management Information Program (Section 1201)

## Slide 13: Overview
WisLCS Use Example:
Third-Party Traffic Information
  Vehicle Navigation Systems
  Phone/Tablet Apps
  Websites
  Social Media
  News Reports

## Slide 14: Overview
WisLCS Use Example:
Oversize/Overweight Permitting - Superload

## Slide 15: Overview
What closures should be entered?
  All let projects
  Design projects (e.g. soil borings, inspections, etc…)
  Planned maintenance
  Planned permit/utility restrictions
  Major special events
  Unplanned emergency lane closures

## Slide 16: Overview
Which roadways is the LCS concerned with?
  Interstates
  US highways
  State highways

## Slide 17: Priority Roadways Southeast Region
I-43
I-94
I-894
US 12
US 41
I-794/WIS 794
US 45
WIS 16
WIS 119
WIS 145
WIS 341

## Slide 18: Priority Roadways Southwest Region
I-39
I-43
I-90
I-94
US 12
US 14
US 41
US 51
US 53
US 151
WIS 26
WIS 30

## Slide 19: Priority Roadways Northwest Region
I-94
I-535
US 53
WIS 29

## Slide 20: Priority Roadways North Central Region
I-39
US 51
US 10
WIS 29

## Slide 21: Priority Roadways Northeast Region
I-43
US 10
US 41
US 45
US 141
US 151
WIS 15
WIS 21
WIS 23
WIS 29
WIS 42
WIS 47
WIS 57
WIS 172
WIS 441

## Slide 22: Users
User Types:
  Maintenance
  Permit
  Construction
  All Types

## Slide 23: Users

## Slide 24: Users
User Acceptance Authorization:
  No Acceptance
  Limited Acceptance (Non-Priority Roadways)
  Full Acceptance (Priority Roadways)

## Slide 25: Users
 | User Types |  |  |  | User Regions |  | Acceptance Authority |  | 
User Roles | Maintenance | Permit | Construction | All Types | One | All | Full | Limited | No
Supervisor*** |  |  |  |  |  |  |  |  | 
Regional Traffic Engineer (RTE) |  |  |  |  |  |  |  |  | 
Statewide Traffic Operations Center (STOC) |  |  |  |  |  |  |  |  | 
Project Manager |  |  |  |  |  |  |  |  | 
Project Leader |  |  |  |  |  |  |  |  | 
Permit Coordinator |  |  |  |  |  |  |  |  | 
Maintenance Coordinator |  |  |  |  |  |  |  |  | 
Requestor |  |  |  |  |  |  |  |  | 
Viewer |  |  |  |  |  |  |  |  | 
Public Information |  |  |  |  |  |  |  |  | 
***Can assign acceptance authority and administrative privileges

## Slide 26: Interfaces
Request, Accept, Modify, Search, Reports

## Slide 27: Home
Menu bar
Past Updates
Messages
Home Page Sections
Notes: Each user will have a different home screen based on the user role.

## Slide 28: Home
Priority Roadway Closures That Need Action
  Role: Supervisor, STOC, and RTE only
  PR closures needing initial acceptance, pending date/time acceptance, and completion
My Closures
  Role: All
  Any closure where you are part of the closure history (e.g. entered, accepted, modified, etc…)
Near Region Boundary Closures
  Role: Supervisor, STOC, and RTE only (region-based)
  Closures where the region is checked in the General Section

## Slide 29: Request
Select the Request link to reach the Request Interface
Choose type of closure

## Slide 30: Request
5 Types of Closures:
  Construction
  Maintenance
  Permit
  Emergency
  Special Events

## Slide 31: Request
Advanced Notification:
Lane closures* | 14 calendar days
Full roadway closures | 14 calendar days
System and service ramp closures* | 14 calendar days
Full system and service ramp closures | 14 calendar days
Project start | 14 calendar days
Construction stage changes | 14 calendar days
Detours | 14 calendar days
Lane closures** | 3 business days
System and service ramp closures** | 3 business days
Modifying all closure types | 3 business days
*With height, weight, or width restrictions (available width, all lanes in one direction ≤16’) | 
** Without height, weight, or width restrictions (available width, all lanes in one direction >16’) | 

## Slide 32: Request
Differences between request forms:
  Revisions to contact info type and required fields
  Emergency closures are automatically accepted upon entry
Construction | Maintenance Emergency Special Event | Permit

## Slide 33: Request
Facility Type:
  3 types to choose from
Mainline | Lane(s) of a highway
Ramp | Service interchange entrance or exit ramp
System Interchange | A ramp from one freeway leading to another freeway

## Slide 34: Request
Duration:
4 types of Duration to choose from
Daily/Nightly | Occurs on a daily or nightly basis as specified by the starting and ending times per each day within the start and end range
Weekly | Occurs on a weekly basis as specified by the day of week dropdowns
Continuous | 24-hour work zone lasting less than 2 weeks
Long Term | Work zone lasting longer than 2 weeks

## Slide 35: Request
Daily/Nightly example:
Cones dropped at 8:00 AM and picked up at 3:00 PM each day for 2 weeks

## Slide 36: Request
Weekly example:
Cones would be dropped at 8:00 AM on Monday and picked up at 3:00 PM on Friday for 2 weeks

## Slide 37: Request
Continuous example:
Cones would be dropped at 8:00 AM on Monday, January 5 and picked up at 3:00 PM on Friday, January 16.

## Slide 38: Request
Long Term example:
Cones would be dropped on January 5 and picked up on January 23.
The end date is typically modified, as the end date gets closer. Long Term closures also need to be completed in the Modify interface when the work is complete.

## Slide 39: Request
Restrictions:
Width, height, and weight restrictions shared with OSOW Permitting group
Future software integration planned

## Slide 40: Request
Oversize/Overweight (OSOW) Permitting Restrictions |  | 
Width | Height | Weight
Available roadway width is required for closures with a duration of 3 calendar days or longer Undivided Roadway = Width from centerline to edge of paved shoulder (up to barrels/barrier) Divided Roadway = Edge of paved shoulder to edge of paved shoulder (up to barrels/barrier) | Minimum vertical clearance through the roadway or restriction in feet (ft/in) Examples: Temporary Signals Structures Profile changes | Maximum vehicle weight allowable through the lane closure in pounds. Examples: Bridge weight posted Road weight posted

## Slide 41: Request
Use field measurements, plan sheets, or other online tools to determine width restrictions
http://www.geodistance.com/

## Slide 42: Accept
The Accept Interface is used to edit or accept closures that have been initially entered into the system but have not yet been accepted.
Only users with authorization may accept closures

## Slide 43: Accept
3 Closure Statuses:

## Slide 44: Modify
The Modify Interface is used to edit, cancel or complete closures that have been previously been accepted.
Access to edit depends on users and roles

## Slide 45: Modify
Date/Time Pending:
Date/Time edited from the Modify interface
Acceptance for Date/Time Pending occurs from the Modify interface (not the Accept interface)
Notes: A user with acceptance authorization will be able to Accept, Reject, Recommend Accept, or Recommend Reject for the pending date/time.

## Slide 46: Modify
When does a closure “Fall Off”?
Any facility that lasts 14 days or more must be manually canceled or completed
Any closure less than 14 days will “fall off” the system when its end date is greater than yesterday.
  Automatically changes from an “active” closures to an “inactive” closure

## Slide 47: Search
The Search interface is used to access all closures within the system.

## Slide 48: Search
LCS Map:
Map the results using the LCS Map button
Prototype functionality only (511 is an alternative option)

## Slide 49: Search
Selecting the MakeLike link allows the user to add another closure with the same General Section attributes (auto-populates the General Section).
Also accessible from the Home page and from the closure request confirmation page

## Slide 50: Reports
Users can use the reports interface as a way to save and print closures that are “active” within the system. Complete all required fields denoted by an asterisk (*).
NOTE: No date ranges
Notes: Active = closure has been or is currently accepted.

## Slide 51: Closure Matrix
CLOSURE STATUS | ACCEPT INTERFACE | MODIFY INTERFACE | SEARCH INTERFACE | REPORTS INTERFACE
ENTERED |  |  |  | 
ACCEPTED |  |  |  | 
CANCELED |  |  |  | 
COMPLETED |  |  |  | 
DELETED | NOTE: Deleted closures are not viewable in any interface |  |  | 

## Slide 52: Additional LCS Resources
511 Local, Calendar, Email, Preferences and Admin Interface

## Slide 53: 511 Local
511 Local is used to report construction closures on local streets ONLY for the 511 Construction Projects website (http://projects.511wi.gov/).
Accessibility depends on user privileges
There is no acceptance process with this interface; closures will automatically be accepted.
Notes: This information is used primarily for public information.

## Slide 54: Calendar
Used for viewing special events (not event closures) that have been entered into the system.
Provides a repository of special events throughout the state to inform personnel requesting or accepting closures of potential events.

## Slide 55: E-mail Interface
Users can sign up to receive daily (3 PM Daily) or weekly (3 PM Friday) e-mail reports by region or county.
Manage a user’s own e-mail reports and/or other (external) e-mail addresses to receive reports.

## Slide 56: Preferences Interface
Preferences allows users to:
Edit Your Account Profile or Password
View Only Access of User Information
View Only Access of Priority Roadways

## Slide 57: Admin
The Admin interface has five links and is only available to those roles that have administrative authorization.

## Slide 58: Support Tools
Documentation, Contacts, Help Tools

## Slide 59: Documentation
http://transportal.cee.wisc.edu/closures/manual.html
User Manual
Quick Reference Guides
PowerPoint Presentations
FAQs

## Slide 60: Help
Additional Help information and documentation is available within the LCS System

## Slide 61: Contacts

## Slide 62: Notifications
Personalize e-mail notifications are sent to users:
Pending/Past Start-Date
  Sent To: Primary/Secondary Contacts
Pending Date/Time
  Sent To: Requestor/Acceptor
Long-Term Closure
  Sent To: Primary/Secondary Contacts
Friday Long-Term Closure
  Sent To: RTEs
Notes: The LCS will send personalized, automated e-mails to users to notify the users of certain conditions. A summary of those e-mail notifications is below.
Pending/Past Start-Date Notice: E-mail sent to the primary and secondary contacts listed in the general section of the closure when the closure is less than two days or past the schedule start date and has not been accepted.
Pending Date/Time E-mail: E-mail sent to the requestor and acceptor of the closure once a pending date/time has been submitted.
Long-Term Closure E-mail: E-mail sent to the primary and secondary contacts listed in the general section of the closure when the long-term closure (greater than 14 days) is within two weeks of the end date and is required to be manually completed.
Friday Long-Term Closure E-mail: E-mail sent to the five regional work zone contacts on a weekly basis to flag closures that are past their end date.

## Slide 63: Training Site
The Training Site is like a sandbox to play with closures. Others may modify previously submitted closures.
May enter the system with different authorization, regions, roles, and types.
http://transportal.cee.wisc.edu/training/WisLCS/Logon.do

## Slide 64: Closure Walk-Through

## Slide 65: Activity